Manual CAT-Control

After power-on → LED test

After Startup → Beep → Error LED ON (Error code = 99)
If you don't press the START Button within 3 minutes (confirm the startup), the CATControl switch to CAT-sensor mode and checks if an active cleaning cycle was interrupted by a power-down.

if NO goto :continue
if YES and settings „Tasklist after power-on if water is in the bowl“ is zero, goto :continue
if YES and cleaning cycle was interruped during scooping -> start cycle with tasklist assigend to CAT-sensor mode
if YES and cleaning cycle was interruped during washing or drying -> start cycle with tasklist entered in settings -> „Tasklist after power-on if water is in the bowl“

:continue

I. Modes

Standard Mode (CARTRIGE-LED = off, CHILD-LOCK-LED = off)
AUTO Click → switch to program (1,2,3,4,CAT)
START Click → Start / Stop cleaning precess

Service Mode (CARTRIDGE-LED = BLINKING)
(from standard mode)
AUTO Longpress + START DoubleClick → Enter service mode (stop cleaning program if running)
AUTO Click → Select output
1 = Drain pump
2 = Bowl
3 = Scopper
4 = Dryer
4 + 1 = Water
4 + 2 = Dosage pump
START Click → switch selected output (1, off, 2)
AUTO Longpress → Exit service mode → reset all outputs
START Longpress → Run into watchdog → all LED's ON → restart after 1 minute

Child Lock (CHILD-LOCK LED = ON)
(from standard mode)
AUTO + START Longpress → Childlock on
AUTO + START Longpress → Childlock off

Lock CATGenie (CARTRIGE-LED = on)
(from standard mode)
START Double-Click to enable
START Double-Click to disable
If CATGenie is more than 1 hour locked, it will unlock automtically.

II. Error Display (ERROR LED = ON)
Error codes (1-7) are shown on the panel in binary form (LED1-LED4)
e.g. Error 1 = LED1, Error 7 = LED4+LED3

Error Codes:
1	Water sensor needs cleaning
2	Water in Bowl on start cleaning
3	Water discharge problem
4	Dryerfuse broken
5	Tasklist not 1-3
6	EEProm tasklist error
9	Unknown error „doCATGenie()“
10	Unknown error „myCATGenie.startCleaning(tasklist)“
11	Error manually set by browser
12	Error manually set by MQTT
99	Power up

A clean watersensor should display an analog value between 50 and 100.

III. Erease Configuration parameter, tasklists and WEB-Page
Press AUTO and START button during LED-Test
-> Errror LED goes ON
-> After EEProm ereased (about 10s) Error LED will flush
Power on/off or wait 60s for watchdog to restart the program with its default values.

IV. Tasklist
* Each tasklist must be a plain ASCII text file

* The first two lines must be
<CATGenie>
tasklist start 1

* the last line must be
tasklist end

* Descriptions have to start with „//“ (No discriptions allowed after a command !!!!)
// Comment

Max. 390 command lines are allowed per tasklist
Max. 5 tasklists are allowed

Possible commands
------------------------
wait 0.6 (seconds)

bowl ccw
bowl cw
bowl stop

scopper up
scopper stop
scopper down

drainpump on
drainpump stop

dospump on
dospump stop

water on
water is on
water waitin 70 (seconds)
water stop
water waitout 1 (seconds)

dryer on
dryer stop

V. What should be improved
- validate tasklist file before download (java downloader)
- check max. web-page size before download (java downloader)